| PAPER SHREDDING |
| --- |
| Hazards Identified | Back & shoulder strain, neck injury due to heavy lid or twisting, and injury to fingers / hands Electrical shock / skin burns / fire from overheating Outlet spark / fire Inhalation of dust Confined space where boxes can fall causing injuries Personal injury from long hair, jewelry or clothing becoming entangled in shredder Finger cuts from staples or paper Hearing loss from machine motor sounds |
| Hazard-Specific Personal Protective Equipment | Not indicated |
| Hazard-Specific Training | Instruction in proper use and care of shredder |
| Related Safe Work Practices and Procedures | Paper Shredding Procedure |
| Safe Work Practice |
| Before using a paper shredder, thoroughly review and understand information provided in the operator’s manual noting the description of safety procedures; Read the Shredding Safe Work Procedure before using the shredder; Inspect shredder for damages or disrepair and the electrical cord and plug for defects; Avoid working in confined spaces such as storage areas to avoid potential injury from falling boxes or other stacked items. Place the shredder at least 4 inches from walls or furniture to allow air to freely flow thorough ventilation slots; Notify your supervisor and remove the shredder from use if any defects are noted; Paper shredders should be used in a well-ventilated area to avoid inhalation of paper dust or wear a paper mask; Always ensure all staples and paper clips are removed from paper before shredding; Always be alert and focused on the shredding task; Place the bag being used to collect shredded papers at least two feet from shredder to prevent a fire. Connect a power bar to the electric cord in order to eliminate reaching when turning the shredder on and off; Rings, jewelry, and Id. tags must be removed before use to prevent being caught in the shredder. (e.g. bracelets, long necklaces) Long hair must be tied back and clothing sleeves, etc. that may get caught in the shredder must be rolled up or secured to prevent being caught in the shredder; Ensure you are ergonomically positioned in front of the shredder to avoid neck, shoulder, or back strain; Keep fingers and hands away from the shredder opening at all times; Limit use of shredder to 5-10 minutes after continuous use of 15 – 30 minutes to prevent machine from overheating and to prevent muscle strains; If the motor overheats, turn the shredder off and allow to cool for at least 15 minutes before using again; Always disconnect the power source before removing and emptying the waste container or when cleaning the shredder; and, Leave the area where the shredder was used in a safe, clean and tidy state. |
| References: | Joint Occupational Health and Safety Committee, Lunenburg County Home Support Services Society: Hazard Analysis, Shredding. Bridgewater, NS, Canada. November 2001. NSC International: Simple Paper Shredder Safety Tips. 2015. Internet Document: http://www.binding.com/paper-shredder-safety-tips Shredder Select. (2015). How to use shredder Effectively Infographic. Retrieved from https://shredderselect.com/#tab-con-13 The Texas Department of Insurance, Division of Workers’ Compensation (TDI/DWC): Paper Shredder Safety Fact Sheet. Texas, USA. June 2006. Internet document: http://www.tdi.state.tx.us/pubs/videoresource/fspapershredder.pdf US Consumer Product Safety Commission: Paper Shredder Safety Alert. N.d. Internet Document: http://www.cpsc.gov/cpscpub/pubs/5127.html |

Note: This safe work practice (SWP) has been provide by Lunenburg Home Support and is intend as a guide for you to develop your organization’s SWP