| PAPER SHREDDING |
| --- |
| Hazards Identified | Back & shoulder strain, neck injury due to heavy lid or twisting, and injury to fingers / hands Electrical shock / skin burns / fire from overheating Outlet spark / fire Inhalation of dust Confined space where boxes can fall causing injuries Personal injury from long hair, jewelry or clothing becoming entangled in shredder Finger cuts from staples or paper Hearing loss from machine motor sounds |
| Hazard-Specific Personal Protective Equipment | Not indicated |
| Hazard-Specific Training | Instruction in proper use and care of shredder |
| Related Safe Work Practices and Procedures | Paper Shredding Practice |
| Safe Work Procedure |
| Set up paper shredder in a well-ventilated, flat, dry area, at least 4 inches from walls or furniture to allow air to freely flow through ventilation slots; Tightly close the bin. Gather other equipment / supplies required: chair, staple remover, large recycling bag; Remove jewelry, rings, and personal Identification tag; Secure hair and clothing to avoid being caught in the shredder; Position recycling bag at least two feet from shredder; Prepare paper for shredding by removing staples, paper clips, etc; Ergonomically position yourself seated in front of the shredder; Turn shredding machine on; Carefully feed small amounts of paper smoothly into shredder, according to manufacturer’s instructions. Never force paper into the shredder; Stop when the container is three-quarters full of shreddings; Turn off machine and unplug or turn off at the power bar; Remove the top section of shredder and set aside. Empty shredded paper into a recycling (blue) bag; Stop shredding for at least 5-10 minutes after continuous use of 15-30 minutes. Reassemble shredder and continue shredding; When finished, turn off machine and unplug or turn off at the power bar and unplug; Remove the top section of shredder again and set aside. Empty shredded paper into the recycling (blue) bag; Reassemble top section of shredder; Store shredder and other equipment/supplies in their proper place; and, Leave the area where it was used in a safe, clean and tidy state. |
| References: | Joint Occupational Health and Safety Committee, Lunenburg County Home Support Services Society: Hazard Analysis, Shredding. Bridgewater, NS, Canada. November 2001. My Binding: How To Use A Paper Shredder In Five Easy Steps. 2015. Internet Document: http://articles.mybinding.com/how-to-use-a-paper-shredder-in-five-easy-steps/# Shredder Select. (2015). How to use shredder Effectively Infographic. Retrieved from https://shredderselect.com/#tab-con-13 The Texas Department of Insurance, Division of Workers’ Compensation (TDI/DWC): Paper Shredder Safety Fact Sheet. Texas, USA. June 2006. Internet document: http://www.tdi.state.tx.us/pubs/videoresource/fspapershredder.pdf US Consumer Product Safety Commission: Paper Shredder Safety Alert. N.d. Internet Document: http://www.cpsc.gov/cpscpub/pubs/5127.html |

Note: This safe work practice (SWP) has been provide by Lunenburg Home Support and is intend as a guide for you to develop your organization’s SWP.